## Slide 1: 3DMIP-MRIQA
David Zhang

## Slide 2: Background
The radiologists are exposed to a huge amount of MRI images each day, only a small part of them can help them make further diagnostic. Most of the MRI datasets are noisy and blurry, we want to create a tool for them to automatically filter out bad MRI datasets and fast select the best MRI datasets using relevant image processing. We can also use MRI with good quality for other tasks e.g. specific organ detection as well as automatic diagnostic.

## Slide 3: Background
Goal for our tool
  high resolution
  small slice distance
  many slices
  wide contrast range
  high sharpness.

## Slide 4: Solution
Background foreground separation of MRI images using Anisotropic Diffusion Filtering Thresholding
Standardized quality metric system for structural brain magnetic resonance images in multi-centering neuroimaging
Slice property by ration of slice thickness by slice distance
Mapping slice number to sigmoid space
Generation of HDR Illumination from a single image for the enhancement of undesirably illuminated images

## Slide 5: Background foreground separation
Used Nonlinear Anisotropic Diffusion Filtering followed by hysteresis thresholding to achieve the desired result. For hysteresis thresholding all we need is High and Low thresholding value. High thresholding value : mean of image after perform Nonlinear Anisotropic Diffusion Filtering Low thresholding value : std of image after perform Nonlinear Anisotropic Diffusion Filtering

## Slide 6: MRI quality metric system
Grayscale image & contrast feature image
a) First grayscale moment grayscale binary image
b) First contrast moment grayscale binary image
c) First contrast moment contrast binary image
d) First grayscale moment contrast binary image
a
b
c
d

## Slide 7: Image quality score
Luminance contrast quality score, q1
Texture quality score, q2
Texture contrast quality score, q3
Lightness quality score, q4
Total = w1 * q1 + w2 * q2 + w3 * q3 + w4 * q4

## Slide 8: Slice property
Slice thickness and slice increment
When the ratio gets 1, the score becomes maximum

## Slide 9: Number property
All dataset slices in the range of [3, 1216]

## Slide 10: Current result
Need to be verified
 | 0.0 | 0.147 | 0.058 | 0.602

## Slide 11: Integrated tool
Dataset input

## Slide 12: Integrated tool
Portable database file

## Slide 13: Thanks